## Slide 1: Numerical simulations of the quadrupole mass analyser in context of its potential application on the Low Velocity Penetrator
Agata Nicolau-Kuklińska
Karol Seweryn
MPSE 2014

## Slide 2: We Are All Made Of Stars
„Of all objects, the planets are those which appear to us under the least varied aspect. We see how we may determine their forms, their distances, their bulk, and their motions, but we can never known anything of their chemical or mineralogical structure; and, much less, that of organized beings living on their surface ...”
Auguste Comte, The Positive Philosophy, Book II, Chapter 1 (1842)

## Slide 3: Mineralogy and chemical composition - important role in the knowledge about Universe
The origin of the Earth's Moon
Hunt for life on Mars
Planning future exploration
Search and mining of space resources
Trevor, R.; Recent developments in isotope-ratio mass spectrometry for geochemistry and cosmochemistry. Rev. Sci. Instrum. 2013, 84, 011101.
Boynton, W., V.; Evidence for Calcium Carbonate at the Mars Phoenix Landing Site. Science, July 2009, vol. 325.
Wanke, H.; Bruckner, J.; Dreibus, G.; Rieder, R.; Ryabchikov, I.: Chemical composition of rocks and soils at the Pathfinder site. Space Sci Rev 2001, 96, 317-330.
Wurz, P.; Abplanalp, D.; Tulej, M.; Iakovleva, M.; Fernandes, V. A.; Chumikov, A.; Managadze, G. G.: Mass spectrometric analysis in planetary science: Investigation of the surface and the atmosphere. Solar Syst Res 2012, 46, 408-422.
Yen, A., S.; An integrated view of the chemistry and mineralogy of martian soils. Nature, July 2005, vol 436.

## Slide 4: Mineralogy and chemical composition - - under surface development
Mass spectrometer
Depth profiling measurements of chemical composition by drill devices or penetrators

## Slide 5: The need for miniaturisation of the mass spectrometer
Benefits:
Low cost launch
Low power consumption
Possibility to place many instruments on board rover or satellite
Possibility to place instrument under surface

## Slide 6: Mass spectrometry - principle of operation
Sample Preparation
Mass
Analyser
Sample
Introduction
Ioniser
Detector
Computer
Inductively Coupled Plasma (ICP)
Electron Impact Ionization (EI)
Chemical Ionization (CI)
Matrix Assisted Laser Desorption Ionization (MALDI)
Laser Desorption Ionisation (LI)
Time-Of-Flight (TOF)
Magnetic Sector
Quadrupole Ion Trap
Quadrupole Mass Analyzer (QMS)

## Slide 7: Qadrupole mass analyser
The a-q stability diagram
q
a
Mass scan line
Udc – DC voltage
Vac – AC voltage
mi - ion mass
r0 - rod radius
ω – angular frequency
e – elektron charge
Ions trajectory
Detector
Quadrupole roads

## Slide 8
Qadrupole mass analyser – geometry
d0 = 2r0 = 4.536 mm
d1 = 1.5 mm
d2 = 9.072 mm
/m
Ref. Gibson, JR.; Taylor, S,; Leck, HJ,: Detailed simulation of mass spectra for quadrupole mass spectrometer systems. J. Vac. Sci. Technol. A 2000, vol. 18, no. 1.
d1
d2
d0
Qadrupole mass analyser - parameters
Name | Value
a | 0.05
q | 0.7
f | 4 MHz
mi | 40 amu
Udc | 9.60 V
Vac | 268.83 V

## Slide 9: Computation of ions propagation
mi = 30 amu
start
end
mi = 10 amu

## Slide 10: Parameters study - frequency

## Slide 11: Parameters study – ion source radius

## Slide 12: Parameters study – initial velocity
Accelerating voltage A = 1 V
Initial ions velocity v = 2245 m/s
Accelerating voltage A = 3 V
Initial ions velocity v = 3889 m/s
Accelerating voltage A = 2 V
Initial ions velocity v = 3175 m/s

## Slide 13: Parameters study – a, q parameter
100%a = 0.05 100%q=0.7 a/q = const

## Slide 14: Parameters study – a, q parameter
a/q = eta = variable

## Slide 15: Future work
Increase the resolution of the quadrupole mass analyser
Optimalisation mass analyser with a smaller size
Miniaturization of other analyser types (e.g. time of flight)
After trade-off of mass spectrometer we plan to build breadbord and integrate with mole penetrator or drill system
fraquency of the ac field
velocity of the ions
geometry of the mass analyser
number of cycles

## Slide 16: Thank you for your attention